# Concepts
of the
SimpleBB

Document version 0.14.

# 1. Basic Information
SimpleBB is an engine of a bulletin board or an internet forum.
The main purpose of a bulletin board or an internet forum is to provide a programmatic way for receiving, storing and serving textual messages of users. The main purpose of this engine is to provide a very simplistic alternative to a popular phpBB bulletin board and forum engine which was written in a very old PHP programming language.
Interaction between a user and this engine is performed via the HTTP protocol between the engine's Gateway module and the user's web browser. Gateway module of the engine provides a public application programming interface (API) which is used for interaction with the engine.
The engine supports an optional front-end part written in JavaScript language which can be used as a lightweight web client to interact with the public API of the engine. Being optional here means that the built-in front-end web client can be disabled in engine's settings. Users of the engine can use their own implementations of the API client when they wish to do so.
# 2. System Modules
System is divided into modules which are represented by micro services. The list of modules is following.

Module	Description
Gateway Module	Accepts incoming HTTPS connections from clients. / Dispatches tasks and makes queries to other modules.
Access Control Module	Registers users and stores their parameters and properties. / Manages user sessions, logs users in and out. / Validates verification codes.
Message Module	Provides access for creating, reading and editing of messages.
Notification Module	Provides access for creating and reading of notifications.
SMTP Module	Sends e-mail messages.
Captcha Module	Creates captchas and verifies user's answers.

Modules communicate with each other using the JSON-RPC M1 protocol. JSON-RPC M1 protocol is a very simple and at the same time very robust protocol for RPC servers. Its specification can be found in its repository: https://vault-thirteen.github.io/JSON-RPC-M1-Specification/
# 3. Messages and Threads
Each message is created by a single user. A message can be edited by its creator, if it is not too old, and by moderators. Message stores information about its creator and time of creation. Message also stores information about its last edit – editor and time of editing.

Main purpose of a message is to store message data – a textual data field which may contain plain text and additional elements encoded with a special BB Code markup language, such as links to images, colourisation of text and other features. Message is an atomic (i.e. not further divisible) unit to store textual information.
## Message parameters
Parameter	Value Type	Description
Id	Integer	Identifier of this message.
ThreadId	Integer	Identifier of a thread containing this message.
Text	String	Textual information of this message.
TextChecksum	Integer	Check sum of the Text field.
Creator.UserId	Integer	ID of a user who created this message.
Creator.Time	Time	Day and time of creation of this message.
Editor.UserId	Integer	ID of a last user who edited this message.
Editor.Time	Time	Day and time of last edit of this message.

Messages are stored in threads. A thread consists of a chain of several messages ordered chronologically.
## Thread parameters
Parameter	Value Type	Description
Id	Integer	Identifier of this thread.
ForumId	Integer	Identifier of a forum containing this thread.
Name	String	Name of this thread.
Messages	Integer Array	List of identifiers of messages of this thread.
Creator.UserId	Integer	ID of a user who created this thread.
Creator.Time	Time	Day and time of creation of this thread.
Editor.UserId	Integer	ID of a last user who edited this thread.
Editor.Time	Time	Day and time of last edit of this thread.

# 4. Forums and Sections
Threads are stored in forums. A forum consists of several threads ordered chronologically.
## Forum parameters
Parameter	Value Type	Description
Id	Integer	Identifier of this forum.
SectionId	Integer	Identifier of a section containing this forum.
Name	String	Name of this forum.
Threads	Integer Array	List of identifiers of threads of this forum.
Creator.UserId	Integer	ID of a user who created this forum.
Creator.Time	Time	Day and time of creation of this forum.
Editor.UserId	Integer	ID of a last user who edited this forum.
Editor.Time	Time	Day and time of last edit of this forum.

Sections are used to divide and group forums into categories or themes. Sections can either hold other sections or a list of forums. A section can not have other sections and forums at the same time, as opposed to later modifications of the phpBB forum engine. Sections do not mix content of different types – either sub-sections only or forums only.
## Section parameters
Parameter	Value Type	Description
Id	Integer	Identifier of a section.
Parent	Integer	Identifier of a parent section containing this section.
ChildType	Integer	Type of child elements: either sub-sections or forums.
Children	Integer Array	List of IDs of child elements (either sub-sections or forums).
Name	String	Name of this section.
Creator.UserId	Integer	ID of a user who created this forum.
Creator.Time	Time	Day and time of creation of this forum.
Editor.UserId	Integer	ID of a last user who edited this forum.
Editor.Time	Time	Day and time of last edit of this forum.

# 5. Notifications
Notifications are short textual messages sent to a specific user of the bulletin board.
## Notification parameters
Parameter	Value Type	Description
Id	Integer	Identifier of the notification.
UserId	Integer	Identifier of a user who this notification is targeted at.
Text	String	Text of the notification.
TimeOfCreation	Time	Day and time of creation of the notification.
IsRead	Boolean	A flag showing whether the user has read this notification or not.
TimeOfReading	Time	Day and time when the user has read the notification for the first time.

Notifications are a one-way method to bring some information to users. Typically, notifications are used to tell users about some system events, such as new replies in a thread, important changes in the system or simply – warnings from administrators.

The following list describes actions which trigger creation of a notification.
## Notification triggers
Object	Action	Recipients
Thread	Change of thread’s parent, i.e. forum.	Users subscribed to the thread.
Thread	Change of thread’s name.	Users subscribed to the thread.
Thread	Deletion of the thread.	Users subscribed to the thread.
Thread & Message	Creation of a new message in the thread.	Users subscribed to the thread.
Thread & Message	Edit of a message in the thread.	Users subscribed to the thread.
Thread & Message	Deletion of a message in the thread.	Users subscribed to the thread.
Thread & Message	Edit of message’s text.	Author of the message.
Thread & Message	Change of message’s parent, i.e. thread.	Author of the message.
Thread & Message	Deletion of the message.	Author of the message.

# 6. Users and Roles
In order to use the system, one should create a registered system user. By default, all the forums and their threads are not visible to unregistered visitors. Users have various access rights to the system depending on their roles. For each kind of possible action or a set of actions there is a separate role. Each user must have one or more roles. Newly registered approved users obtain the simplest role – Reader. Unregistered or unapproved users do not have the Reader role. List of possible user roles is described below.
## User role list
User Role	Description
Administrator	Can create, edit, move and delete sections. / Can create, edit, move and delete forums. / Can edit, move and delete threads. / Can move and delete messages. / Can create and delete notifications. / Can view user parameters and set user roles.
Moderator	Can edit messages. / Can ban and unban users.
Author	Can create new threads.
Writer	Can add new messages into a thread*. / Can edit its own messages when they are not too old.
Reader	Can read sections, forums, threads and messages. / Can subscribe to thread events.
Logged user	Can read notifications. / Can view logged users, user's log status. / Can view user's roles.

[*] – Writer can add new messages into a thread when there is no collision with the latest message in the thread. This means that if the latest message in the thread can be edited by an ordinary (non-moderator) writer, the writer can not add a new message and should edit the latest message instead.
## User action matrix
The following matrix describes which activities are allowed and forbidden for separate user roles.
Meaning: O = action is allowed (can), - = action is not defined (can not).

Category	Action	Administrator	Moderator	Author	Writer	Reader	Logged user
Section	Create	O	-	-	-	-	-
	Read	-	-	-	-	O	-
	Edit (rename)	O	-	-	-	-	-
	Move	O	-	-	-	-	-
	Delete	O	-	-	-	-	-
Forum	Create	O	-	-	-	-	-
	Read	-	-	-	-	O	-
	Edit (rename)	O	-	-	-	-	-
	Move	O	-	-	-	-	-
	Delete	O	-	-	-	-	-
Thread	Create	-	-	O	-	-	-
	Read	-	-	-	-	O	-
	Edit (rename)	O	-	-	-	-	-
	Move	O	-	-	-	-	-
	Delete	O	-	-	-	-	-
Message	Create	-	-	-	O	-	-
	Read	-	-	-	-	O	-
	Edit (change text)	-	O	-	O*	-	-
	Move	O	-	-	-	-	-
	Delete	O	-	-	-	-	-
Notification	Create	O	-	-	-	-	-
	Read	-	-	-	-	-	O*
	Delete	O*	-	-	-	-	-
User	View list of logged users	-	-	-	-	-	O
	View logged status	-	-	-	-	-	O
	View user roles	-	-	-	-	-	O
	View user parameters	O	-	-	-	-	-
	Set user roles	O	-	-	-	-	-
	Ban	-	O	-	-	-	-
	Unban	-	O	-	-	-	-
Subscription	Create	-	-	-	-	O	-
	Delete	-	-	-	-	O	-

Notes:
* – Writer can edit only its own messages and only for a specified period of time.
* – Logged User can read only those notifications which were sent to him/her.
* – Administrator can delete only those notifications which were read by a user.
# 7. Access Control Module
Access Control Module supports functionality related to user registration, logging users in and out of the system, user session management and control of access to various parts of the system. Access Control Module is used mostly by other system modules – other modules make requests to ACM and ACM provides response to them.

When a user successfully logs into the system, a session is started. When a user logs out of the system, a session is deleted. Each user may have only a single session, i.e. multiple sessions per user are forbidden. Each session is automatically closed when it is too long.

Access Control Module provides following functionality.
## Access control module functions
C	Function	Description
P	Ping	Service liveness.
R	RegisterUser	User registration.
	GetListOfRegistrationsReadyForApproval	Gets the list of requests for registration which are ready to be approved, i.e. verified by e-mail.
	RejectRegistrationRequest	Rejects the registration request.
	ApproveAndRegisterUser	User approval and registration. For administrators only.
L	LogUserIn	Logs the user into the system.
	LogUserOut	Logs the user out of the system by the user.
	LogUserOutA	Logs the user out of the system by the administrator.
	GetListOfLoggedUsers	Shows a list of users who are currently logged into the system.
	GetListOfLoggedUsersOnPage	Shows a paginated list of users who are currently logged into the system.
	GetListOfAllUsers	Shows a list of all users of the system.
	GetListOfAllUsersOnPage	Shows a paginated list of all users of the system.
	IsUserLoggedIn	Checks whether the specified user is logged in or not.
V	ChangePassword	Changes user's password.
	ChangeEmail	Changes user's e-mail address.
	GetUserSession	Gets user’s session.
P	GetUserName	Reads user’s name.
	GetUserRoles	Returns a list of user's roles.
	ViewUserParameters	Returns visible parameters of a user.
	SetUserRoleAuthor	Changes user's IsAuthor parameter.
	SetUserRoleWriter	Changes user's IsWriter parameter.
	SetUserRoleReader	Changes user's IsReader parameter.
	GetSelfRoles	Returns roles of the current user.
B	BanUser	Bans a user.
	UnbanUser	Unbans a user.
O	ShowDiagnosticData	Shows diagnostic information.
	Test*	Performs a test.

[*] – Function is available only in debug mode.

Every user of a forum starts using the system with registration. To gain access to the system after registration a user must log into the system. Registration, logging and other work flows or scenarios are described in a separate file.
## Pre-registered user properties
Following user properties are temporarily used for pre-registered users.

Property	Value Type	Description
Id	Integer	Identifier of a user.
PreRegTime	Time	Day and time of pre-registration in the system.
Email	String	E-mail address of a user.
VerificationCode	String	A verification code, sent to the user.
IsEmailSent	Boolean	Email send status.
IsEmailApproved	Boolean	True for an approved e-mail address, False otherwise.
Name	String	Public name or nickname visible to other users.
Password	String	Password. This field is never shown to clients.
IsReadyForApproval	Boolean	True for a user which is ready to be approved, False otherwise.
IsApproved	Boolean	True for an approved user, False otherwise.
ApprovalTime	Time	Day and time of the approval.

## User properties
Properties of a user are following.

Property	Value Type	Description
Id	Integer	Identifier of a user.
PreRegTime	Time	Day and time of pre-registration in the system.
Email	String	E-mail address of a user.
Name	String	Public name or nickname visible to other users.
Password	String	Password. This field is never shown to clients.
ApprovalTime	Time	Day and time of the approval.
RegTime	Time	Day and time of registration in the system.
Roles	Object	User roles.
LastBadLogInTime	Time	Time of the last unsuccessful log-in attempt.
BanTime	Time	Day and time of user's last ban in the system. This field is not reset to Null when a user is unbanned.
LastBadActionTime	Time	Time of the last unsuccessful action, such as password change, e-mail address change and other important actions.

## Roles’ properties
Properties of user roles are following.

Property	Value Type	Description
IsAdministrator	Boolean	Indicator of the Administrator role.
IsModerator	Boolean	Indicator of the Moderator role.
IsAuthor	Boolean	Indicator of the Author role.
IsWriter	Boolean	Indicator of the Writer role.
IsReader	Boolean	Indicator of the Reader role.
CanLogIn	Boolean	Can log into the system. True for normal users. False for banned users.

## Preliminary session parameters
Parameter	Value Type	Description
Id	Integer	Preliminary session Id.
UserId	Integer	Id of a user who initiated the session.
TimeOfCreation	Time	Day and time of session's creation.
RequestId	String	A unique Id of a request to log in. It prevents hi-jacking the session by other users.
UserIPAB	Integer	User's IP address as an array of bytes.
AuthDataBytes	Bytes	Binary data (several bytes) used for authentication process.
IsCaptchaRequired	Boolean	A flag showing that a user must solve a captcha.
CaptchaId	String	Id of a captcha task.
IsVerifiedByCaptcha	Boolean	A flag showing that a user has solved a captcha.
IsVerifiedByPassword	Boolean	A flag showing that a user has entered a correct password.
VerificationCode	String	Verification code sent to a user.
IsEmailSent	Boolean	Email send status.
IsVerifiedByEmail	Boolean	A flag showing that a user has been verified via an e-mail message.

## Session parameters
Parameter	Value Type	Description
Id	Integer	Normal session Id.
UserId	Integer	Id of a user who started the session.
StartTime	Time	Day and time of session's start, i.e. user's successful log in.
UserIPAB	Bytes	User's IP address as an array of bytes.

## System settings
Following system settings are available for the ACM module.
Setting	Description
SiteName*	Name of the site where this forum engine works.
SiteDomain*	Domain name of the site where this forum engine works.
VerificationCodeLength	Length of verification codes sent by e-mail.
UserNameMaxLenInBytes	Maximum size of user name in bytes.
UserPasswordMaxLenInBytes	Maximum size of a packed user password in bytes.
PreRegUserExpirationTime	Time (duration in seconds) after which a pre-registered user having no approved e-mail address is deleted from the system.
IsAdminApprovalRequired	If set to True, each user should be manually approved by administrators before registration.
LogInRequestIdLength	Length of request IDs for user logging in.
LogInTryTimeout	Time which a user must wait after an unsuccessful log-in attempt. If a user continues to log in earlier than this timeout, it must solve an additional captcha. This setting is set in seconds. Recommended value: 60.
PreSessionExpirationTime	Time (duration in seconds) after which an abandoned preliminary session is deleted from the system.
SessionMaxDuration*	Maximum duration of a session. If a session is longer than this parameter, it is automatically closed. This setting is set in seconds. Recommended value: 86'400 (24 hours).
PasswordChangeExpirationTime	Time (duration in seconds) after which an abandoned request to change password is deleted from the system.
EmailChangeExpirationTime	Time (duration in seconds) after which an abandoned request to change electronic mail address is deleted from the system.
ActionTryTimeout	Time which a user must wait after an unsuccessful important action. If a user continues to perform important actions earlier than this timeout, it must solve an additional captcha. This setting is set in seconds. Recommended value: 60.
PageSize	Size of a page for listing requests. Recommended value: 20.
IsTableOfIncidentsUsed	A flag which enables table of incidents. This setting must be synchronised with the firewall of the Gateway module.
BlockTimePerIncident	A set of configurations of block time per each incident type. In seconds.
IsDebugMode	Debug mode flag.

[*] - This setting must be synchronised with the Gateway module.
# 8. SMTP Module
The SMTP Module sends e-mail messages and has following functions.
## SMTP module functions
C	Function	Description
P	Ping	Service liveness.
M	SendMessage	Sends an e-mail message to a specified recipient.
O	ShowDiagnosticData	Shows diagnostic information.

## System settings
Following system settings are available for the SMTP module.
Setting	Description
IsDebugMode	Debug mode flag.

# 9. Captcha Module
The Captcha Module deals with captcha riddles and has following functions.
## Captcha module functions
C	Function	Description
P	Ping	Service liveness.
C	CreateCaptcha	Creates a random captcha image.
	CheckCaptcha	Checks the provided captcha answer.
	GetImage*	Shows a captcha image.
O	ShowDiagnosticData	Shows diagnostic information.

[*] – Functionality of showing images is configurable – it may be either integrated into the CreateCaptcha function or be a stand-alone separate function which is accessed with a separate method.
## System settings
Following system settings are available for the Captcha module.
Setting	Description
IsDebugMode	Debug mode flag.

# 10. Message Module
The Message Module deals with messages, threads, forums, sections and has following functions.
## Message module functions
C	Function	Description
P	Ping	Service liveness.
S	AddSection	Adds a new section into another section or as a root section.
	ChangeSectionName	Changes section's name.
	ChangeSectionParent	Moves a non-root section from an old section into a new section.
	GetSection	Returns a section specified by its ID.
	MoveSectionUp	Moves the section one position up in its parent.
	MoveSectionDown	Moves the section one position down in its parent.
	DeleteSection	Deletes an existing empty section.
F	AddForum	Adds a new forum into a section.
	ChangeForumName	Changes forum's name.
	ChangeForumSection	Moves a forum from an old section into a new section.
	GetForum	Returns a forum specified by its ID.
	MoveForumUp	Moves the forum one position up in its parent.
	MoveForumDown	Moves the forum one position down in its parent.
	DeleteForum	Deletes an existing empty forum.
T	AddThread	Adds a new thread into an existing forum.
	ChangeThreadName	Changes thread's name.
	ChangeThreadForum	Moves a thread from an old forum into a new forum.
	GetThread	Returns a thread specified by its ID.
	GetThreadNamesByIds	Returns names of threads specified by their IDs.
	MoveThreadUp	Moves the thread one position up in its parent.
	MoveThreadDown	Moves the thread one position down in its parent.
	DeleteThread	Deletes an existing empty thread of a forum.
	ThreadExistsS	Checks whether the specified thread exists or not. This method is used by the system.
M	AddMessage	Adds a new message into an existing thread.
	ChangeMessageText	Changes message's text.
	ChangeMessageThread	Moves a message from an old thread into a new thread.
	GetMessage	Returns a message specified by its ID.
	GetLatestMessageOfThread	Returns the latest message of a thread by its ID.
	DeleteMessage	Deletes an existing message of a thread.
C	ListThreadAndMessages	Returns a thread with all its messages.
	ListThreadAndMessagesOnPage	Returns a thread with messages on a specified page.
	ListForumAndThreads	Returns a forum with all its threads.
	ListForumAndThreadsOnPage	Returns a forum with threads on a specified page.
	ListSectionsAndForums	Returns a list of all sections and forums.
O	GetDKey	Gets the DKey.
	ShowDiagnosticData	Shows diagnostic information.
	Test*	Performs a test.

[*] – Function is available only in debug mode.
## System settings
Following system settings are available for the Message module.
Setting	Description
DKeySize	Size of a DKey.
MessageEditTime*	Maximum allowed message age, i.e. time passed after message creation, when message editing is allowed. This setting is used for simple user roles and does not apply to moderators who can edit messages of any age. Is set in seconds.
PageSize*	Page size for pagination of items.
NewThreadsAtTop	This parameter controls how new and updated threads are placed inside forums. If set to True, then following will happen: / New threads will be added to the start (top) of the list of forum's threads instead of being added to the end (bottom) of the list; / New messages added to threads will update the thread moving it to the start (top) position of the list of forum's threads. / If set to False, then new threads are added to the end (bottom) of the list and thread's new messages do not update thread's position in the list.
IsDebugMode	Debug mode flag.

[*] - This setting must be synchronised with other modules.
# 11. Notification Module
The Notification Module deals with notifications created by the system or administrators and directed to specific users of the bulletin board.
## Notification module functions
C	Function	Description
P	Ping	Service liveness.
S	AddNotification	Creates a new notification for a user. This method is used to send notifications by administrators.
	AddNotificationS	Creates a new notification for a user. This method is used to send notifications by the system.
	SendNotificationIfPossibleS	Tries to send a notification to a user when it is possible. This method is used by the system.
	GetNotification	Reads a single notification.
	GetNotifications	Reads all notifications for a user.
	GetNotificationsOnPage	Reads paginated notifications for a user.
	GetUnreadNotifications	Reads all unread notifications for a user.
	CountUnreadNotifications	Counts all unread notifications for a user.
	MarkNotificationAsRead	Marks a notifications as read.
	DeleteNotification	Deletes a notification.
O	ProcessSystemEventS	Processes a system event. This method is used by the system.
	GetDKey	Gets the DKey.
	ShowDiagnosticData	Shows diagnostic information.
	Test*	Performs a test.

[*] – Function is available only in debug mode.
## System settings
Following system settings are available for the Notification module.
Setting	Description
NotificationTtl	Lifetime of a read notification. Is set in seconds.
NotificationCountLimit	Maximum number of unread notification allowed.
PageSize*	Page size for pagination of items.
DKeySize	Size of a DKey.
IsTableOfIncidentsUsed	A flag which enables table of incidents. This setting must be synchronised with the firewall of the Gateway module.
BlockTimePerIncident	A set of configurations of block time per each incident type. In seconds.
IsDebugMode	Debug mode flag.

[*] - This setting must be synchronised with other modules.
# 12. Subscription Module
The Subscription Module deals with subscriptions. Users of the system can subscribe to threads and get notifications about these threads.
## Subscription module functions
C	Function	Description
P	Ping	Service liveness.
S	AddSubscription	Creates a new subscription for a user.
	IsSelfSubscribed	Checks whether the caller user has a subscription to the thread.
	IsUserSubscribed	Checks whether the user has a subscription to the thread.
	IsUserSubscribedS	Checks whether the user has a subscription to the thread. This method is used by the system.
	CountSelfSubscriptions	Counts subscriptions of the current user.
	GetSelfSubscriptions	Reads a list of subscriptions of the current user.
	GetSelfSubscriptionsOnPage	Reads a paginated list of subscriptions of the current user.
	GetUserSubscriptions	Reads a list of user’s subscriptions.
	GetUserSubscriptionsOnPage	Reads a paginated list of user’s subscriptions.
	GetThreadSubscribersS	Reads a list of users subscribed to the specified thread. This method is used by the system.
	DeleteSelfSubscription	Deletes a user’s self subscription.
	DeleteSubscription	Deletes a user’s subscription.
	DeleteSubscriptionS	Deletes a user’s subscription. This method is used by the system.
	ClearThreadSubscriptionsS	Clears subscriptions of an existing thread. This method is used by the system.
O	GetDKey	Gets the DKey.
	ShowDiagnosticData	Shows diagnostic information.
	Test*	Performs a test.

[*] – Function is available only in debug mode.
## System settings
Following system settings are available for the Subscription module.
Setting	Description
PageSize*	Page size for pagination of items.
DKeySize	Size of a DKey.
IsDebugMode	Debug mode flag.

[*] - This setting must be synchronised with other modules.
# 13. Gateway Module
Gateway Module accepts incoming HTTPS connections from external clients, dispatches tasks and makes queries to other modules. Gateway Module also acts as a network firewall, restricting access to those clients who have been blocked. In order to act as a firewall, the Gateway Module contains a list of blocked IP addresses. This list may be changed by the Access Control Module with the help of JSON RPC M1 protocol.
Incoming requests made by external clients via the HTTPS protocol are first analysed by their IP address. Those requests which are made from unblocked IP addresses are redirected to other modules, such as ACM or Message Module, depending on their contents.
The following list of internal functions is supported by the Gateway Module.
## Gateway module internal functions
C	Function	Description
P	Ping	Service liveness.
I	BlockIPAddress	Adds an IP address to a block list or updates an existing record.
	IsIPAddressBlocked	Checks whether the specified IP address is blocked or not.
O	ShowDiagnosticData	Shows diagnostic information.

## System settings
Following system settings are available for the Gateway module.
Setting	Description
SettingsVersion	Version number of API settings.
SiteName*	Name of the site where this forum engine works.
SiteDomain*	Domain name of the site where this forum engine works.
IsFirewallUsed	A flag which enables firewall. This setting must be synchronised with the table of incidents of the ACM module.
ClientIPAddressSource	This setting selects where to search for client's IP address. '1' means that IP address is taken directly from the client's address of the HTTP request; '2' means that IP address is taken from the custom HTTP header which is configured by the ClientIPAddressHeader setting.
ClientIPAddressHeader	Name of a custom HTTP header used as a source of client's IP address. This setting is used only when ClientIPAddressSource is set to '2'.
CaptchaImgServerHost*	Host name of the server providing captcha images.
CaptchaImgServerPort*	Port number of the server providing captcha images.
CaptchaFolder	An URL folder of the captcha handler. Recommended value: "captcha".
SessionMaxDuration*	Maximum duration of a session.
MessageEditTime*	Maximum allowed message age, i.e. time passed after message creation, when message editing is allowed. This setting is used for simple user roles and does not apply to moderators who can edit messages of any age. Is set in seconds.
PageSize*	Page size for pagination of items.
ApiFolder	An URL folder of the system API. Recommended value: "api".
PublicSettingsFileName	Name of a virtual file containing public settings of the product. Typical name is "settings.json".
IsFrontEndEnabled**	A flag which enables the front end part of the system.
FrontEndStaticFilesFolder	An URL folder containing static files required for functioning of the front end part. Recommended value: "fe".
FrontEndAssetsFolder	Path to a local folder containing front end assets. Typical path is "assets\frontend".
IsDebugMode	Debug mode flag.
IsDeveloperMode	Developer mode flag.
DevModeHttpHeaderAccessControlAllowOrigin	Value of the HTTP 'Access-Control-Allow-Origin' header for the developer mode.
NotificationCountLimit*	Maximum number of unread notification allowed.

[*] - This setting must be synchronised with other modules.
[**] – Front end is the part of the system which serves HTML files, JavaScript scripts, static files and other assets required to load the initial web page which makes requests to the API of the system. This front end is optional, i.e. it may be switched off. Usually you switch off the built-in front end part when you need to use an external front end implemented in a separate application, such as a mobile or a desktop client application written in C#, Java or any other programming language.
# 14. Technical characteristics
Below are described some of the technical characteristics of the SimpleBB bulletin board engine.
## Difference between phpBB and SimpleBB
SimpleBB is written in Go programming language and uses micro service architecture.
If you are used to the phpBB forum and PHP programming language itself, there are several major differences between phpBB and SimpleBB which must be noted.
1. PHP programming language is a scripting language. It is used for interpreted scripts, not for compiled programs.
2. PHP programming language is not used for persistent runtime executables. PHP scripts are executed from time to time. Programs written with Go language instead are always running in the background as all normal executable programs and services do.
3. PHP programming language does not allow modularity and separation of a product into several services. Go language encourages creation of products which consist of several separate services.
Though various programming languages have a lot in common, PHP language does not allow to write programs which are compact and easy to maintain because all products written in PHP are monolithic.
It is also worth mentioning that programs written in micro service style (or architecture) have a drawback, which did not exist in phpBB – micro services are difficult to start and stop. Moreover, communication between micro services requires additional efforts from developers and testers. So, if you are a PHP person, you will find this product a little bit strange at first time.
The SimpleBB engine accepts clients' requests and provides response in a more convenient ways than those old school scripts written in PHP. Every time you use phpBB, it flushes a big bucket of cold water on you, and this water consists of huge HTML pages at which you can stare for hours searching for something. The SimpleBB engine provides response in a much easier way – it shows you a quite compact and convenient JSON file which is easy to read and understand. Data taken from JSON files can be easily parsed and used with a front end written in JavaScript, Java, C# or any other programming language of your taste.
## Scaling
SimpleBB forum engine uses a very simplistic approach to everything, and scaling is not an exception. The engine allows each server to be run only in a single instance. This is done in order to make everything simple and robust.
## Logics
All the logics is used on an application level. Logics is almost not used on the level of SQL database server and this done on purpose – this makes the product very simple, easy to maintain and reliable.
As the logics is used on the application level, all the database locks are made on the same level – application level – making it easy and safe to recover after system crashes. If a database access was locked while the application crashed, the lock disappears after the application is shut down or restarted.
There is also another peculiarity of locks made on application level – it is nearly impossible to use SQL transactions mixed with logics on an application level. Technically, SQL forbids to return multiple results (inserted row IDs and affected row counts) in a complex transaction, forcing programmers to move all the application logics to the SQL database level. In most cases this leads to difficulties of code inspections and debugging, while Go language and SQL language are totally different programming languages.
This product is very simple and requires no knowledge of writing ugly and monster-like functions and procedures in specific dialects of SQL languages. This approach allows an easy porting of the product to other database management systems if such a requirement arises in future.
However, there is a small disadvantage of such an approach. If a system crashes while a complex action is in progress, some junk may be left in the database that will need a little bit of manual cleaning. Comparing with those monster-like SQL procedures that try to suck all the application logics in themselves, it is much easier to clean a redundant database entry than to support all the SQL dialects.
## Reliability
The simplicity of the product can also be seen in its data models used on the database level. Each object of important class is linked from both sides – a parent object stores a link to a child object and vice versa – a child object stores a link to a parent object. This approach makes it very easy to restore database after failures and check consistency in case of a system crash. This means that it is always possible to repair the database in case of a system crash. In other words, the SimpleBB forum engine uses redundancy as a safe guard for data consistency.
Another example is the inability to remove parent objects which have child objects attached, e.g. it is not possible to remove a forum which has threads inside of it. This safe guard requires additional efforts to remove content but makes the system more safe and reliable.
System's important roles such as Moderator and Administrator are protected from all the system users, i.e. it is not possible to gain access to these roles using the API. Such roles are attached to users in a configuration file of the ACM module. No such feature was used in the phpBB forum engine as far as we know.
## Installation and configuration
The SimpleBB engine does not have installation scripts as phpBB forum engine does. All the installation process is comprised of creation of configuration files.
To configure or re-configure the product each module or micro service must be configured or re-configured separately. Configuration is done by editing of configuration files. To apply new configuration of a module or a micro service it must be restarted.